Peterson MIDI Resource SystemTM with an Ahlborn Archive Module1

Programming piston (patch) changes in the MIDI Resource SystemTM that will operate an Ahlborn Archive Module1 is accomplished as follows:

Program the Ahlborn Archive Module1

1. Program the Ahlborn Archive Module1 presets with the desired voices for each manual. (Refer to the            Ahlborn Archive Module1 Instruction Manual for details.)

There are 6 presets and 5 memory levels for a total of 30 presets. Each of these 30 presets can be 	programmed with any of the voices on any division. Thus the presets can be considered "General Pistons".

2. Select the desired Memory Level (A-E) using the "MEM" button, then turn on the desired stop(s), next press 	and hold the Set ("S") button and finally press the desired Preset button (1-6).

3. Repeat this process for each of the Ahlborn Archive Module1 presets.

Note: Be sure the Ahlborn Archive Module1 MIDI channels are programmed to use channels 9 for Swell, 10            for Great, 11 for Choir (AUX), 12 for Pedal and channel 16 for "Common".

Program the MIDI Resource SystemTM

1. Program the MIDI Resource SystemTM pistons (or Pre-Set Stops) by first setting the Prog/Use/Show switch 	in Program Mode.

2. First, one layer must be programmed to select the Ahlborn1 preset. Any manual number can used here. The 	channel number must be set to 16 and the program number selects the Ahlborn Archive Module1 preset.

Note: You must add one to the Ahlborn Archive Module1 preset numbers (and add six for each memory level) 	      to find the required program number.  i.e. Memory Level A - Preset #1 = 2;  Memory Level B - Preset            #2 = (2+1+6 =) 9.   (Caution: Do not use program numbers 32-128 as unexpected results may occur.)

3. Then push and hold the Organ's (MIDI) Set button followed by the desired piston button. The MIDI        Resource SystemTM control panel should display "set" in the program number window.

4. Next, tap a key on the desired manual (to set the Manual #), then using the Channel Up/Down switch set     the desired channel number. The channel numbers to be used are Channel 9 for Swell, 10 for Great, 	11 for Choir and 12 for Pedal. (These channels allow using the sound module along with sequencing the 	organ-- the organ uses channels 1-7 for record playback.) Then using the Program Up/Down set the 	program number to 1. (The program number selected here can be any number except 0.)

5. Then push and hold the Organ's (MIDI) Set button followed by the desired piston button. The MIDI        Resource SystemTM control panel should display "set" in the program number window.

6. If more than one manual is to be played from this preset, repeat the above steps (4-5) for each manual.

An example layered piston could be set as follows:

Man#  Ch#  Prg#

1       16      6        Ahlborn1 preset #5 (Mem A) selected on channel 16

1         9      1        Swell playing on MIDI channel  9

2       10      1        Great playing on MIDI channel 10

4       12      1        Pedal playing on MIDI channel 12

7. Repeat this process (1-6) for each of the desired MIDI Resource SystemTM pistons.

1. Ahlborn Archive is a trademark of Generalmusic, Marignano, Italy.