Setting up an Allen Organ Co. "Smart Sequencer" for

use with the PETERSON MIDI Resource SystemTM

When using an Allen Organ Co. "Smart Sequencer" with the PETERSON MIDI Resource SystemTM, channels must be reassigned in the "Smart Sequencer" to match those being used by the MIDI Resource SystemTM.

This is accomplished by:

1. Push and hold the "MIDI" button on the "Smart Sequencer" front     panel for 7-8 seconds. The set-up mode is active when the front     panel display changes.

2. Use the Up/Down buttons to select the MIDI channel for each        manual.

3. Press the "MIDI" button again to change manuals.

The manual/channel assignments must be set as follows for use with the MIDI Resource SystemTM:

Chan.	Manual

1		Swell

2		Great

3		Choir

4		Pedal

5		Solo

Additional information can be obtained directly from the Allen Organ Co. by calling 610-966-2200.

Allen Organ Co. and "Smart Sequencer" are trademarks of Allen Organ Co., Macungie PA